## Slide 1
Goals: Hadron 3s-separation between 3 - 50 GeV/c
Complement electron ID below 15 GeV/c
Cover forward pseudorapidity 1.5 (barrel) - 3.5 (b. pipe)
dRICH Features:
Extended 3-50 GeV/c momentum range --> Dual radiator
Single-photon detection in high Bfield --> SiPM
Limited space --> Compact optics with curved detector
ePIC dRICH
Dual-radiator Ring-imaging Cherenkov Detector (dRICH)
Essential to access flavor information
4m
1

## Slide 2
dRICH Radiators
Active Area = 21605 cm2
Dead Area = 3269 cm2 (13%)
Wasted Area = 9112 cm2 (27 %)
Active Area = 21368 cm2
Dead Area = 3506 cm2 (14%)
Wasted Area = 1868 cm2 (7 %)
Large demonstrators delivered – Wall engineering ongoing
Aerogel with n=1.026 validated with lab and prototype tests
Goal
Sonar to measure speed of sound
10 bar chamber + specrophotometer to measure
light transmission in the visible range
Jamin interferometer for precise n determination
C2F6 validated with lab & prototype tests
Design of online purity monitors ongoing
2
Notes: Come si arriva ai 1.8 Tbps ? 3 KHz / 3(shutter) * 3e5 (canali) *64

## Slide 3
dRICH Photo Sensor Engineering
Testing new Hamamatsu sensors after
- 109 neq
- oven annealing
UV enhanced
Time resolution with ALCOR redout
Details of in-situ annealing protocol based on Joule-effect
75 mm
50 mm
Photon yield
3
FInalization of the engineering of the SiPM optimized layout and temperature treatments ongoing
Notes: Come si arriva ai 1.8 Tbps ? 3 KHz / 3(shutter) * 3e5 (canali) *64

## Slide 4
Readout Board (RDO)
Delivery imminent
dRICH Readout Electronic
Carrier v3
Front-End Board (FEB)
Design of the readout electronics in the “final” ePIC layout version is ready for test production.
Test-production started ‘Jan 25
Proton irradiation campaigns for ALCOR-32 and key RDO components showed SEU rate is within the expected manageable levels
A working DAQ scheme has been identified to support ML online data filtering at sub-detector level against pure dark-count event
4
Silicon die layout
Compact ball-grid array (BGA) package with interposer
MPW run in March ‘25
ALCOR v3 – 64 channels
Notes: N ties smaller than ePIC!

## Slide 5
Real Scale Prototype
5
Aerogel support
CFRP Layer
composition
Mirror mounting and alignment (aka NA62)
Engineering of all the mechanical details pursued with the real-scale prototype and component demonstrators
PO issued
Vessel

## Slide 6
INFN Funding Profile
6
Assumptions: - Installation in 2032
- possibility to split the major procurements in batches/years
Potential risk: - sub-optimal spreading of vendor effort for SiPM
- late investment on aerogel
Sensors
Electronics
Radiators
Mechanics
R&D
Peak investment being mitigated with respect 2024 anticipation
2024
60% Preliminary Design Review passed. A construction and QA plan is outlined accounting for lead, assembling and commissioning time

## Slide 7
dRICH Online Filtering
Scheme based on ePIC DAM (Felix) &
APEIRON communication network (INFN)
Preliminary tests
7
A working DAQ scheme has been identified to support ML online data filtering at sub-detector level against pure dark-count event
detector integrated analysis
sub-sector integrated analysis
Classifier
The feasibility of a scintillating fiber layer operated as a charged particle tagger is being studied
Notes: Farsi spieare la latenza. Bisogna sapere ul data rate a cui sono arrivati (factor 2?)

## Slide 8
Photon Detector Unit
50 mm
75 mm
+ SiPM carrierv3
+ RDO
8
/26
Full size engineering
test article
2025
2026
+ ALCOR 64ch
+ FEB 64
Steadly progress of photodetector towards integrated design completion in 2026
ALCOR 32 ch
Notes: Come si arriva ai 1.8 Tbps ? 3 KHz / 3(shutter) * 3e5 (canali) *64

## Slide 9
Test Beams
Previous validations:
Dual-radiator concept
C2F6 radiator gas performance
Aerogel rafractive index
SiPM-ALCOR readout chain
EIC-drive readout plane
Temperature gradients
2025 main goals:
Real scale 1-sector prototype
with demo components
ALCOR readout with RDO
9
Slot at SPS H8 in November
2025