## Slide 1
dRICH: effective solution for ePIC detector
Two radiators: Aerogel (nAERO~1.02) + Gas (nC2F6 ~ 1.0008)
SiPM Detector: 0.5 m2/sector , 3x3 mm2 pixel
Phase Space:
- Polar angle: 5-25 deg
Momentum: 3-60 GeV/c
Dual Radiator RICH @ EIC
Two main : cover wide momentum range 3 - 60 GeV/c
challenges work in high (~ 1T) magnetic field
1

## Slide 2
dRICH Prototype - MAPMTs
2
Operative prototype commissioned. Double ring imaging achieved. Performance in line
with expectations except for aerogel single-photon angular resolution (worse by a factor ~ 1.5)
Gas ring coverage: 60%
Aerogel ring coverage: 40 %
Reference readout from CLAS12 RICH:
H13700 MA-PMTs + ALCOR3 ToT chip
Two radiator concept validation
(with a reference MAPMT readout)

## Slide 3
dRICH Prototype - SiPM
3
Gas vessel
Detector box
Aerogel box
Aerogel rings of 8 GeV negative pions
Successful Cherenkov ring detection with SiPM
- irradiated
(with protons up to 1010 neq)
- annealed
(in oven at 150 C)
Irradiation and annealing campaign performed on various SiPM sensor from different manufacturers
Test beam at CERN PS
dRICH prototype with SiPM+ALCOR readout

## Slide 4
EIC-driven Readout Plane
4
4x SiPM matrix arrays
(256 channels)
flex PCB
minicrate with
fron-end electronics
(ALCOR ASIC inside)
cooling stack
(water-cooled Peltier)
aerogel tile
(not shown)
cables and services
(not shown)
Compact 256 ch unit with integrated cooling and annealing capability
14 cm
ALCOR v2
ToT architecture, streaming mode ready
50 ps time bin
500 kHz rate per channel
cryogenic compatible

## Slide 5
EIC-driven Readout Plane
5
Compact 256 ch unit with integrated cooling and annealing capability
Photon Detector Unit (PDU)
Readout Box (front)
Instrumented with more than 1000 channels
Readout Box (top)
20 x 20 x 20 cm3
14 cm long

## Slide 6
dRICH Prototype – EIC readout
6
DAQ and DCS computers
auxiliary control electronics crates
low voltage and high voltage power supplies
gigabit ETH switch for DAQ and DCS
dRICH prototype
SiPM photodetector readout box
DAQ FPGAs and clock distribution
Beam test at CERN PS-T10 beam line: October 2023

## Slide 7
dRICH Prototype – EIC readout
7
8 GeV positive beam
aerogel
pions
aerogel
protons
C2F6
pions
Online monitors and QA plots indicate a successful beam test. Analysis is ongoing
low temperature SiPM operation
10 GeV positive beam
C2F6 gas
aerogel
Successful imaging with a compact
EIC-driven readout plane
based on SiPM + ALCOR

## Slide 8
Status and Plans
8
2022: dRICH imaging with reference detectors
Extended SiPM irradiation + annealing campaign
Cherenkov light detection with irradiated SiPM
2023: EIC-drive photon-detector plane
dRICH imaging with EIC-driven detector plane
Outlook: Refined data analysis and simulation
Final assessment