## Slide 1
dRICH: flexible configuration (JLEIC, ePHENIX)
Radiators: Aerogel (nAERO~1.02) + Gas (nC2F6 ~ 1.0008)
Detector: 0.5 m2/sector , 3x3 mm2 pixel
Single-photon detection in ~1T magnetic field
Outside acceptance, reduced constraints
 best candidate for SiPM option
Phase Space:
- Polar angle: 5-25 deg
Momentum: 3-60 GeV/c
Dual Radiator RICH in EIC Hadron-endcap
ePHENIX
JLEIC
Hit on detector
Photon impact
on mirror(s)

## Slide 2
dRICH Feasibility Study
Aerogel SPE
Gas SPE
Refractive index / UV filters
Gap length / Sensor surface
Studied with full Geant4 simulation, with Bayesian L. Barion et al., JINST 15 (2020) 02, C02040
optimization and analytic parameterizations E. Cisbani et al., JINST 15 (2020) 05, P05009
Compact and cost-effective solution for continuous momentum coverage (3-60 GeV/c)
Strong interest in the dRICH electron-pion separation capability
e-p
p-k
p-k

## Slide 3
dRICH Prototype
Dual radiator imaging
Pressure vessel for gas & n tune
Sensor & readout friendly
4 x H13700
Kaon
4 GeV/c
Kaon
15 GeV/c
Kaon
25 GeV/c

## Slide 4
SiPM Program
SiPM: sampled for vendor, type and dose (at groups of 4)
organized in 8 x 4 matrices for imaging
to be irradiated up to 1011 neq/cm2
ALCOR: ASICS under development at INFN:
ToT architecture for cryogenic application
32 channels, 50 ps TDC, >500 kHz/channel
Readout: bias distributors and signal pre-conditioning
compatible with temperature treatments,
laboratory characterization, and firefly
high-data rate DAQ
Imaging test with dRICH prototype
Readout test with ALCOR chip
Laboratory characterization