## Slide 1
Flavor Separation Instruments for Nucleon Tomography
M. Contalbrigo – INFN Ferrara
Aperitivi Scientifici
25th October 2019,
Dip. Fisica and Astronomia, Bologna
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 2
2
Contalbrigo M.
Longitudinal momentum
k+=xP+
l
l
Photon Virtuality
Q2
d2kT
d2bT
d2kT
d2bT
High Energy Probe
Hard Scale
The Nucleon Structure
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Discutere che servono spin (fin dall’iniio  metter qualche simbolo nel disegno ?) e scala perturbativa

## Slide 3
3
Contalbrigo M.
H-W Lin++ [1711.07916]
Kinematic Coverage
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Mettere quello per polarizzato ?

## Slide 4
4
Contalbrigo M.
MMHT [arXiv 1412.3989]
HERAPDF2.0 [arXiv 1506.06042]
CT14 [arXiv 1506.07443]
CJ15 [arXiv 1602.03154]
ABMP16 [arXiv 1701.05838]
NNPDF3.1 [arXiv 1706.00428]
BB [arXiv 1005.3113]
LSS [arXiv 1010.0574]
DSSV [arXiv 1404.4293]
BS [arXiv 1408.7057]
NNPDF [arXiv 1406.5539]
JLAM [arXiv 1601.07782]
H-W Lin++ [1711.07916]
Parton Content
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: RICH: contributo a Delta_g > 0 con jets e pi0, contributo a Delta_qbar con W+/-
Mettere una slide per hadronici ?

## Slide 5
5
Contalbrigo M.
Unpolarized moments
Polarized (helicity) moments
H-W Lin++ [1711.07916]
Parton Content & Lattice
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Vedere come fanno la media fra le varie PDF
JAM17 a parte in Delta_q perche’ non impone gA SU(3) e fitta PDF/FF insieme
Baccehtta parla di rinormalizzazione non completa e parte di calcoli ancora pertubativa …. Non e’ che e’ il mare ?
Lattice could be used for extrapolation in unmeasured regins!!

## Slide 6
6
Contalbrigo M.
H1 [arXiv: 1611.03421]
Good perturbative description
(hard gluon emission)
pT>5 GeV Q2>5 GeV2
Part in a pT<<Q TMD regime
Inclusive Jets @HERA
Flavor Sensitive Instruments, 245d October 2019, Bologna

## Slide 7
7
Dynamic Spin
- Parton polarization
- Orbital motion
- Form Factors
- Magnetic Moment
Color charge density
- Nucleon tomography
- Diffractive physics
- Gluon saturation
- Color force
Hadronization
Spin-orbit effects
Parton energy loss
- Jet quenching
Parton Correlations
- dPDFs
- Short range
- MPI
The Strong Force Confined Universe
Flavor Sensitive Instruments, 245d October 2019, Bologna

## Slide 8
8
Contalbrigo M.
Longitudinal momentum
k+=xP+
l
l
Photon Virtuality
Q2
d2kT
d2bT
d2kT
d2bT
High Energy Probe
Hard Scale
The 3D Nucleon Structure
Confinement Scale
Transverse plane
kT
bT
Transverse momentum
Transverse position
Spin
Contalbrigo M.
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Discutere che servono spin (fin dall’iniio  metter qualche simbolo nel disegno ?) e scala perturbativa

## Slide 9
Parton kinematics and flavor from observed hadron kinematics and type
Access to:
3D momentum and spin-orbit effect:
Distribution and fragmentation convoluted:
9
Contalbrigo M.
SIDIS & TMDs
Contalbrigo M.
Flavor Sensitive Instruments, 245d October 2019, Bologna
TMDs: Transverse Momentum Parton Distributions

## Slide 10
10
A. Bacchetta++ [arXiv:1703.10157]
TMDs
+9 / -6 (TMDs)
ATLAS++ [arXiv:1701.07240]
Unpolarised TMDs
Contalbrigo M.
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Bacchetta reference!

## Slide 11
11
Sivers from polarized SIDIS
HERMES [arXiv:0906.3918]
COMPASS [arXiv:1205.5122]
x
Yoon++ [arXiv: 1706.03406]
Spin-Orbit Effects: Sivers
11
Contalbrigo M.
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: oCapire storia del segno
Che modello segue AFTER ?

## Slide 12
12
Contalbrigo M.
Babar [arXiv 1309.5278]
BESIII [arXiv 1507.06824]
Belle [talk at DIS2014]
HERMES [arXiv 0408013]
COMPASS [arXiv 1005.5609]
COMPASS [arXiv 1408.4405]
HERMES [arXiv 0906.3918]
Q2 ~ 110 GeV2
Q2 ~ 5-7 GeV2
Spin-Orbit Effects: Collins
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Aggiungere riferimenti

## Slide 13
13
Distributions:
Charges:
A. Bacchetta @ DIS219
Helicity
Transversity & Tensor Charge
Flavor Sensitive Instruments, 245d October 2019, Bologna
Contalbrigo M.
x
x
Notes: Trova quale e’ Lattice ed eventualmente che modelli

## Slide 14
14
Baessler++ @ this Conf.
Bychkov++ [arXiv:0804.1815]
Pattie++ [arXiv:1309.2499]
Flavor Sensitive Instruments, 245d October 2019, Bologna
Tensor Charge & BSM Physics
Contalbrigo M.
EDM violates P and T and CP (if CPT holds)
Notes: Mettere il plot con confronto low energy vs LHC!!
Mettere il caso pi0 ?

## Slide 15
15
Contalbrigo M.
Thomas Jefferson National Accelerator Facility, Newport News, VA, USA
6  12 GeV Beam
Jefferson Lab
Flavor Sensitive Instruments, 245d October 2019, Bologna

## Slide 16
16
Contalbrigo M.
10 m
Large acceptance spectrometer. Operative since 02/18
Main INFN contributions to CLAS12: FT, RICH, HDice
CLAS12 in Hall-B
Flavor Sensitive Instruments, 245d October 2019, Bologna

## Slide 17
17
Contalbrigo M.
INSTITUTIONS
INFN (Italy) Bari, Ferrara, Genova, L.Frascati, Roma/ISS
Jefferson Lab (Newport News, USA)
Argonne National Lab (Argonne, USA)
Duquesne University (Pittsburgh, USA)
George Washington University (USA)
Glasgow University (Glasgow, UK)
Kyungpook National University, (Daegu, Korea)
University of Connecticut (Storrs, USA)
UTFSM (Valparaiso, Chile)
Cherenkov angle (mrad)
7 Gev/c
6 Gev/c
8 Gev/c
p
k
p
Goal kaon-pion separation up to 8 GeV/c (prototype results):
CLAS12 RICH
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 18
18
Contalbrigo M.
Aeronautic technology for structure
to maximize lightness and stiffness. Trapezoid of composite materials: CFRP inside acceptance, Aluminum outside
Carbon Fiber Mirrors (spherical)
to maximize lightness and stiffness. Consolidate technology (HERMES, AMS, LHCb) but ~ 30 % material budget reduction
RICH Components
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Immagine electronic panel e scheda ottica

## Slide 19
19
Contalbrigo M.
World leading transparency
At such large n and volumes
Glass-Skin Mirrors (planar)
Innovative technology never used in nuclear experiments.
1.5 mm outside, 0.7 mm inside acceptance
~ 1/5 cost for squared meter vs CFRP
Large refractive index aerogel radiator
Tiles up to 20x20x3 cm2 at n=1.05.
RICH Components
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Immagine electronic panel e scheda ottica

## Slide 20
20
80 H8500 + 350 H12700
< 1 cm spatial resolution
< 1 ns time resolution
Compatible with the low torus fringe field
Average MA-PMT gain ~ 2.7 106
Corresponds to SPE ~ 400 fC
✓ 64 6x6 mm2 pixels cost effective device
✓ High sensitivity on VIS towards UV light
✓ Mature and reliable technology
✓ Large Area (5x5 cm2)
✓ High packing density (89 %)
✓ Fast response
✓ Expensive technology
~ 1 m2 active surface
Photo Sensor: MA-PMT
Contalbrigo M.
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Dire meglio chi fa cosa.

## Slide 21
21
Contalbrigo M.
Readout Electronics
Compact (matches sensor area)
Modular Front-End (Mechanical adapter, ASIC, FPGA)
Scalable fiber optic DAQ (TCP/IP or SSP)
Tessellated (common HV, LV and optical fiber)
SSP Fiber-Optic DAQ
Tile power dissipation ~ 3.5 W
HV
LV
Optical
Fiber
RICH Readout Electronics
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Immagine electronic panel e scheda ottica

## Slide 22
22
Contalbrigo M.
Analog: Charge (1 fC)
Digital: Time (1 ns)
Trigger latency (8 ms)
Optical ethernet (2.5 Gbps)
Trigger: external
internal
self
On-board pulser
Contalbrigo M.
Charge
Test
Test pulse
Slow shaper
Slow shaper
Digital pulse
Linear response
Multiplexed readout
Limited holding time delays
Used for calibrations
RICH Front-End Electronics
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Aggiungere range di validita’ per fattorizzazione GPDs

## Slide 23
23
Multiplexed readout up to 50 kHz
High resolution SPE spectrum
Viable for efficiency and gain monitors
In conjunction with timing, allows the
study of PMT discharge and cross-talk
Contalbrigo M.
Gain
ADC Charge Measurement
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Dire meglio chi fa cosa.

## Slide 24
24
Contalbrigo M.
Analog: Charge (1 fC)
Digital: Time (1 ns)
Trigger latency (8 ms)
Optical ethernet (2.5 Gbps)
Trigger: external
internal
self
On-board pulser
Contalbrigo M.
Start time
Stop time
Test
Test pulse
Slow shaper
Slow shaper
Digital pulse
Digital response
Working in saturated regime
64 parallel channel readout
8 ms FIFO and delays
1 ns time resolution
RICH Front-End Electronics
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Aggiungere range di validita’ per fattorizzazione GPDs

## Slide 25
25
Pedestal rms as seen by a test-point
As seen by RICH readout
During Acceptance tests
During Internal Pulser Calibration
Discrimination down to 20 fC, i.e. few % of SPE, allows sensor characterization
Contalbrigo M.
Flavor Sensitive Instruments, 245d October 2019, Bologna
TDC Digital Readout
Notes: Vedere presentazione Matteo

## Slide 26
26
Sensor
Electronic
Gain x 4
THR ~ 1/80 SPE
Signal
Cross-talk
Sampling time
Contalbrigo M.
Flavor Sensitive Instruments, 245d October 2019, Bologna
Optical and Electric Cross-talk
Notes: Dire meglio chi fa cosa.

## Slide 27
Threshold
Eff. ratio
0 0.5 1 2 4
Eff. ratio
Maroc
Gain
Relative efficiency map
Relative gain map
x ¼
x ½ MAROC
x 1 GAIN
x 2
x 4
27
Contalbrigo M.
Flavor Sensitive Instruments, 245d October 2019, Bologna
Single Photon Discrimination
Notes: Mettere relazione con blue luminosity ?

## Slide 28
28
Contalbrigo M.
Flavor Sensitive Instruments, 245d October 2019, Bologna
RICH Installation
January 2018
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 29
Contalbrigo M.
Pedestal rms [DAC unit]: without and with grounding grid
Jan 18
-- off
-- 1000 V
Mar 18
-- off
-- 1000 V
Pixel #
Pixel
Pixel #
Pixel #
Pixel
Pixel
Electronic Pedestal
29
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 30
30
Contalbrigo M.
After equalization: distributions narrower and less sensitive to the common threshold
saturate signals and cross-talk well separate
Flavor Sensitive Instruments, 245d October 2019, Bologna
Online Equalization
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 31
31
Contalbrigo M.
Dark counts
Other bunch
CLAS12 Reconstructed Time and Position:
Photons are traced using information
from other CLAS12 detectors
RICH Measured Time and Position:
Defined by the RICH DAQ
Good photons should match
in time and space
Time analysis allows to
separate spurious signals
Flavor Sensitive Instruments, 245d October 2019, Bologna
Single Photon Time Analysis
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 32
32
Contalbrigo M.
Flavor Sensitive Instruments, 245d October 2019, Bologna
Time Offsets
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 33
33
Contalbrigo M.
PMT 270
s = 0.58 ns
PMT 52
s = 0.66 ns
before time-walk correction
after time-walk correction
Single-photon time resolution better than the 1 ns specification
Flavor Sensitive Instruments, 245d October 2019, Bologna
Single Photon Time Resolution
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 34
34
Contalbrigo M.
Flavor Sensitive Instruments, 245d October 2019, Bologna
Single Photon Time Resolution
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 35
35
Contalbrigo M.
Analytic solution for direct photons
“Exact” solution for the Cherenkov Angle
Only direct photons
Ray traced solution for direct photons
Assume knowledge of aerogel ref index
Any photon
GOAL: get a Cherenkov angle estimate for each photon for detailed PID optimization
Flavor Sensitive Instruments, 245d October 2019, Bologna
Cherenkov Angle Reconstruction
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 36
36
Contalbrigo M.
Flavor Sensitive Instruments, 245d October 2019, Bologna
Cherenkov Angle Reconstruction
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 37
37
Contalbrigo M.
RGA data, direct photons No alignment of internal components
Number of photons and single photon resolution close to TDR
4.5 mrad
Raw RICH alignment (not for internal components)
TDR: ~ 18 Npe
TDR:
~ 4.5 mrad
Flavor Sensitive Instruments, 245d October 2019, Bologna
Cherenkov Angle Resolution
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 38
38
Contalbrigo M.
Hadron separation, direct photon, RGA data, raw alignment
PRELIMINARY
Flavor Sensitive Instruments, 245d October 2019, Bologna
Hadron Separation
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 39
39
Contalbrigo M.
H12700 +
CLAS12
readout
J. Stevens @ DIRC19
Application: DIRC @ GlueX
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Dire meglio chi fa cosa.

## Slide 40
40
Contalbrigo M.
40
Contalbrigo M.
JLEIC
The Future: EIC
The ultimate machine fro QCD
Well Beyond HERA:
x 1000 Lumi
Variable CM energy
Polarized Beams
Ion Beam
Precision Detectors
CD0 + Site Decision
Expected Soon
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Aggiungere range di validita’ per fattorizzazione GPDs

## Slide 41
Scattered electron
Particles associated with struck parton
Partecle associated with initial ion
Resolve partons in nucleons
  high beam energies and luminosities
  Q2 up to ~1000 GeV2
Need to resolve quantities (kt, bt) of the order a few hundred MeV in the proton
Correlated quantitites, multi-D analyses
 High Granularity, wide dynamic range
Need to detect all types of remnants
to seek for correlations:
  scattered electron
  particles associated with initial ion
  particles associated with struck parton
Large acceptance, Forward particle
detection, Excellent PID
Specific requirements to move
beyond the longitudinal description
41
Contalbrigo M.
EIC Detector Challenges
Flavor Sensitive Instruments, 245d October 2019, Bologna

## Slide 42
e-endcap:
medium momentum (< 10 GeV/c)
aerogel modular Cherenkov
h-endcap:
medium and high momentum (3-50 GeV/c)
dual radiator Cherenkov
Sensors
Workign at 1 T magnetic field ?
Radiation Tolerant ?
42
Contalbrigo M.
Asymmetric detector
Compact solutions to contain the cost
New high-tech materials
New technologies with emerging markets
in medical imaging and homeland security
Activity linked to eRD14 EIC R&D consortium
Particle Identification @ EIC
Flavor Sensitive Instruments, 245d October 2019, Bologna

## Slide 43
43
Contalbrigo M.
Flavor Sensitive Instruments, 245d October 2019, Bologna
Next PID Solutions: Modular RICH
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 44
Next PID Solutions: Modular RICH
mRICH: An aerogel RICH with Fresnel lens focalization for compact and projective imaging
p/K sepration up to ~ 10 GeV/c
Compact / modular solution for few-GeV range
Aerogel
Fresnel lens
Sensor plane
44
Contalbrigo M.
Flavor Sensitive Instruments, 245d October 2019, Bologna
Proposed also for sPHENIX @ BNL

## Slide 45
45
Contalbrigo M.
mRICH Test Beam
Flavor Sensitive Instruments, 245d October 2019, Bologna
H13700 to reach the 3 mm spatial resolution
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 46
46
Contalbrigo M.
Solution optimized for JLEIC
Next PID Solutions: Dual Radiator RICH
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 47
Dual RICH So Far
47
Contalbrigo M.
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 48
Commercial vacuum technology for safety and cost effectiveness
Overlapping rings for parallel beam particles
dRICH Prototype Design
Gas Exchange
Aerogel Conf.
48
Contalbrigo M.
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 49
dRICH Prototype Performance
Filters to study and
control chromatic
dispersion
Aerogel
Gas
(2.9)
(0.5)
(0.5)
(0.8)
(1.2)
(0.5)
Montecarlo simulation
@EIC
@EIC
49
Contalbrigo M.
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 50
Readout Independent element
for flexibility: supports various
detectors with integrated cooling
Reference:
MAROC + SSP/VSX
Dedicated:
SiREAD + SSP/ethernet
Sensors Reference B-field tolerant:
MA-PMTs MCP-PMTs (LAPPDs) SiPMs
Development: Sensor and Readout
50
Contalbrigo M.
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 51
51
Contalbrigo M.
Pixel #
Pixel #
Peltier cell cooling
Down to -30o in N2
Development: SiPMs
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 52
Paolo Carniti
@ RICH 2018
I. Balossino et al.
NIMA 876 (2017) 89
T. Tsang et al.
JINST 11 (2016) P12002
T= 84 K
109 neq cm2
Annealing at 250 oC
T= 0 C
few 109 neq cm2
52
Contalbrigo M.
SiPM Radiation Tolerance
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 53
53
Contalbrigo M.
Flavor Sensitive Instruments, 245d October 2019, Bologna
Development: SiREAD Chip (HU)
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 54
54
Contalbrigo M.
Optical ethernet (2.5 Gbps)
Small setups:
TCP/IP
Optical bridge / PC Desktop
Full experiment:
SSP protocol
SSP board / VSX crate
Next:
Ethernet Switches
Contalbrigo M.
SSP board / VSX crate
2 RICH sectors ~ 50 k channels
Optical bridge / PC Desktop
Few FPGA units ~ 500 channels
Flavor Sensitive Instruments, 245d October 2019, Bologna
Development: Back-End (JLab)
Notes: Aggiungere range di validita’ per fattorizzazione GPDs

## Slide 55
55
Contalbrigo M.
EIC
Data in the much needed “intermediate” energy region matching “pure” pQCD with “pure” TMD regime.
JLab12
Nucleon Structure Landscape
Flavor Sensitive Instruments, 245d October 2019, Bologna

## Slide 56
56
Contalbrigo M.
The Next QCD Frontier
EIC (and JLab) is a unique opportunity
for a comprehensive QCD study
and possible breakthroughs
Potential impact on many
fields of investigation
EIC offers immediate opportunities
for supported R&D activities
on science and technology
56
Contalbrigo M.
PID is crucial to achieve
flavor separation
Seek for cost-effective
solutions with potential application
In other fields
Executive Summary
Flavor Sensitive Instruments, 245d October 2019, Bologna
Notes: Aggiungere range di validita’ per fattorizzazione GPDs

## Slide 57
Laser head +
diffuser
MAPMT holder
JLab
632 nm picosecond pulsed laser light
Light diffuser to illuminate the whole MAPMT surface
Standardized system with CLAS12 electronics
H8500 6x6 mm2 pixel sensor so far
INFN
632 nm and 407 nm picosecond pulsed laser light
Light concentrator to scan the sensor surface
Flexible layout supporting various sensors and
Front-End electronics
Detailed characterization
Sensors: gain, efficiency, cross-talk, radiation tolerance
Electronics: gain, cross-talk, thresholds, time resolution
Laser head +
collimator
MAPMT holder
57
Contalbrigo M.
Flavor Sensitive Instruments, 245d October 2019, Bologna
Pulsed Laser Test Benches
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 58
Very pure HD gas is needed to produce polarized targets.
Raman spectrosopy is used to analyze the content of H2 and D2 contaminants in the HD gas.
58
Contalbrigo M.
HDice: Frozen Spin Polarized Target
Advantages:
Dilution factors ~ 1
Low holding magnetic fields
FE: frozen B field on a
bulk SC MgB2 magnet
Polarized targets of solid HD in frozen spin mode.
Longitudinal and Transverse Polarizations: up to 60% H or 35% D.
Physics program rated as High-Impact by PAC41
RM1: dewars & cryostats
HD gas purity by Raman
distillation and analysis
CSN3, Torino 9 settembre 2020
ML