## Slide 1
dRICH: effective solution, part of EIC reference detector
Radiators: Aerogel (nAERO~1.02) + Gas (nC2F6 ~ 1.0008)
Detector: 0.5 m2/sector , 3x3 mm2 pixel.  SiPM option
Phase Space:
- Polar angle: 5-25 deg
Momentum: 3-60 GeV/c
Dual Radiator RICH @ EIC
Two challenges: cover wide momentum range 3 - 60 GeV/c
work in high (~ 1T) magnetic field

## Slide 2
Dual radiator imaging
Pressure vessel for gas & n tune
Sensor & readout friendly
Goals:
Study dual radiator performance and interplay
Study specifications and alternatives for optical components
Test alternate single-photon detection systems
* First test-beams in September and October ‘21 at CERN (in synergy with ALICE at PS T10)
dRICH Prototype

## Slide 3
dRICH Setup
Photo detector
  Gas volume
Inner mirror
Aerogel
Trackign GEM
Cooling

## Slide 4
Use large area H13700 coupled to CLAS12 RICH MAROC front-end
Allows to study the working principles and optical performance of the components
DATA p+
12 GeV/c
MC p+
12 GeV/c
4 x H13700
dRICH Online: Imaging
Trigger area
by GEM

## Slide 5
dRICH Online: SiPM Readout
Test Cherenkov application for magnetic field insensitive sensor (SiPM)
Control SiPM high dark count to isolate single photon signal (same amplitude!)
Use a new ALCOR chip (high-rate ToT architecture) in streaming mode
30 mm
15 mm
Reflected signal moves with mirror
Time coincidence with beam particle
Cherenkov ring
SiPM
Sensor

## Slide 6
SiPM Irradiation Campaign
6
TIFPA
Proton
Beam
Facility
Collimated
Beam
109-1011 neq
Before
After
Climate chamber
Various SiPM

## Slide 7
Status and Plans
7
2021: MC simulations
First SiPM irradiation + annealing campaign
Basic dRICH prototype
First dRICH test-beam with hadron beams (commissioning)
2022: Extended SiPM irradiation + annealing campaign
Improved prototype
Second test-beam campaign (realistic performance)
Data analysis and technical note (D24.3)
2023: Refined data analysis and simulation
Third test-beam campaign (component optimization)
Final assessment towardds TDR