## Slide 1
EIC Dual-Radiator RICH
EPIC PID Review
Contalbrigo Marco – INFN Ferrara
Title
dRICH Collaboration
EIC forward RICH
dRICH Baseline Design
dRICH Organization
dRICH Layout
dRICH Gas Radiator
dRICH Aerogel Radiator
dRICH Mirrors
EPIC Environment
dRICH Photo-detector
dRICH Readout Scheme
dRICH Services
dRICH Simulation: Sensors Model
dRICH Simulation: Aerogel Model
dRICH Simulation: Resolution
dRICH Simulation: Momentum Reach
18. R&D: Status
R&D: Highlight
R&D: Milestones
dRICH Construction Schedule
Optimization & Risk Mitigation
Environment, Safety & Healt
Quality Assurance
Calibration & Commissioning
Executive Summary
Charge 1
Charge 2
Charge 3
Charge 4 & 5 see Integration talk
Charge 6

## Slide 2
dRICH Collaboration
2
EIC PID Review - 5th July 2023
BA, BO, CS, CT, FE ,
GE, LNF, LNS, RM2,
SA, TO, TS
EPIC
Compact cost-effective solution for particle identification in the high-energy endcap at EIC
EIC RICH Consortium
…..
dRICH
CLAS12 RICH COMPASS RICH ALICE HMPID DARKSIDE ALCOR
Background Expertise:

## Slide 3
3
EIC Forward RICH
Forward particle detection
Hadron ID in the extended 3-50 GeV/c interval
Support electron ID up to 15 GeV/c
Essential for semi-inclusive physics
due to absence of kinematics constraints at event-level
EIC PID Review - 5th July 2023

## Slide 4
dRICH Baseline Design
4
dRICH: cost-effective compact solution
Radiators: Aerogel (nAERO~1.02) + Gas (nC2F6 ~ 1.0008)
Detector: 0.5 m2/sector, 3x3 mm2 pixel  SiPM option
Main cover wide momentum range 3 - 50 GeV/c
features work in high (~ 1T) magnetic field
fit in a quite limited (for a gas RICH) space
ATHENA case
EIC PID Review - 5th July 2023

## Slide 5
Cooling Level-5
Vessel Level-5
Detector box Level-5
Mirror Alignment Level-5
dRICH Organization
5
6.10.04 Particle Identification Level-3
6.10.04.03 dRICH Level-4
CAM from Project
CAM from Project + DSTC from EPIC (M. Contalbrigo)
Photo-Detector Level-5
Work packages lead from EPIC
Front-end Asics Level-5
Data-acquisition Level-5
Mechanics Level-5
Gas radiator Level-5
Mirror Level-5
Aerogel Radiator Level-5
R. Preghenella, INFN-BO, INFN-FE, INFN-CS, INFN-SA, INFN-LNF, INFN-CT, NISER
F. Cossio, INFN-TO, INFN-BO
P. Antonioli, INFN-BO, INFN-FE
A. Saputi, INFN-FE, INFN-CT, INFN-GE, JLAB, BNL
F. Tessarotto, INFN-TS, BNL
A. Vossen, DUKE, INFN-FE
G. Volpe, INFN-BA, INFN-FE, RICH Consortium
C. Chatterjee, INFN-TS, DUKE, INFN-FE, RICH Consort.
Simulation
Slow Control Level-5
Work packages not yet active
Interlock Level-5
Power Supply Level-5
dRICH Meeting - 19th July 2023
Notes: Significant INFN in-kind

## Slide 6
dRICH Layout
6
Windows: sandwich panel made of two ~1 mm carbon fiber reinforced epoxy skins separated by 30 mm PMI foam or Al honeycomb (~ 1% X0)
Shells: 3 mm (inner tube) to 8 mm (outer tube) thick carbon fiber epoxy composite (~ 4% X0)
Skins formed with two layers of balanced weave laminate with fibers at 0o/90o and +/- 45o for uniform stiffness
EIC PID Review - 5th July 2023

## Slide 7
dRICH Gas Radiator
7
C2F6
Chromaticity
Assume dRICH volume ~ 20 m3
C2F6 density 5.73 Kg/m3  114 kg
Initial minimal quantity ~ 200 kg
~ 500 kg could be enough for 10 yr of operation
Initial survey:
30 kg /yr emission  300 tCO2 /yr
comparable to one intercontinental flight /yr
New standards should reduce significantly the losses and
environmental impact
EIC PID Review - 5th July 2023

## Slide 8
dRICH Aerogel Radiator
8
Aerogel Factory (BELLE-II)
Initial evaluation & Reproducibility
on small samples in sinergy with ALICE
Touch Probe: planarity and thickness
10x10x2 cm3 tile
(from ALICE)
Laser spot broadening: Y profile
No aerogel
3 x 2 cm aerogel
Density & refractive index
Transmittance & Transflectance
0.3 mm
5 mm pass
EIC PID Review - 5th July 2023
Notes: Menzionare Temple via RICH Consortium

## Slide 9
dRICH Mirrors
9
CMA Carbon fiber mirrors (HERMES, AMS, LHCb, CLAS12)
cost-effective light & stiff solution:
roughness driven by mandrel 1-2 nm rms
surface accuracy better than 0.2 mrad
radius reproducibility better than 1 %
CLAS12 RICH QA laboratory
@ JLab being refurnished
EIC PID Review - 5th July 2023
3.5 m
Mirror aberrations
Notes: Menzionare coating e SBU ?

## Slide 10
EPIC Environment
10
ePIC background group
beam-beam interactions only
1-MeV neutron equivalent fluence (1 fb-1 ep running)
Strong (~ 0.7 T) magnetic field, not uniform
Moderate radiation level (~ 1010 neq/cm2 after 1000 fb-1)
SiPM with low-T (< -30 C) working point and high-T (~ 150 C) annealing cycles
Benchmark fluence (10 x)
~ 107 1-MeV neq/cm2 / fb-1
EIC PID Review - 5th July 2023
SiPM talk
Notes: Aggiungere distribuzioni in numero fotoni ?

## Slide 11
dRICH Photo-Detector
11
Photon Detector Unit (PDU):
Compact to minimize space
4x Hamamatsu S13361-3050HS SiPM arrays
4x Front-End Boards (FEB)
4x ALCOR chip (ToT discrimination)
4 x Annealing Circuitry
1x Read-Out Board (RDO)
1x Cooling plate (< -30 C)
Active area is shaped to resemble the focal surface and best exploits the focalization
Detector box:
Shaped to fit the space
Quartz window
Cooling for sensors and electronics
Power distributing patch panel
Heat insulation
Heat exchanger
Cold plate
SiPM array
Back-side
connectors
FEB
(ALCOR)
Service
connections
RDO
Flex PCB
SiPM array
ALCOR chip
EIC PID Review - 5th July 2023
12 cm
Notes: Capire quanto veloce va il chip (definizione shutter)

## Slide 12
dRICH Readout Scheme
12
Master
4992 4992 1248 312 312 (x4) 14 (x2) 6
up to 1.8 Tbps
up to 18 Gbps
PDU
I level DAM
II level DAM
Experiment Electronic trailer
Reduce complexity at the detector level (spare space, custom boards, FPGA/SEU)
Maximise modularity (detector shaping) and capability (data stream)
DAM Hierarchy: Maximum data rate capability till DAM-L1
Big data reduction at DAM-L1 with external input (2 ms latency interaction tagger)
DAM-L2 data aggregation per sector allows for effective data-reduction algorithms
DAM-L1 might be eventually stored in the experimental Hall (rack enclosure)
Sensor FEB RDO RDO
shutter
interaction tagger
data filter
EIC PID Review - 5th July 2023
3 300 kHz DCR/ch
to EPIC
Notes: Come si arriva ai 1.8 Tbps ? 3 KHz / 3(shutter) * 3e5 (canali) *64

## Slide 13
Existing systems
& standards:
COMPASS
C4F10 recirculating
and purging system
dRICH Services
13
Commercial Power supply Cooling plants
Examples:
EIC PID Review - 5th July 2023

## Slide 14
dRICH Simulation: Sensor Model
14
Realistic description accounting for material budget
Photon detection efficiency
EIC PID Review - 5th July 2023
x 0.7 global efficiency factor

## Slide 15
dRICH Simulation: Aerogel Model
15
Comparison DATA vs MC model
DATA: Aerogel Factory samples
MC: EPIC parameterization
Chromatic dispersion
(major expected contribution to resolution)
Absorption length
MC
DATA
MC
DATA
Scattering length
Data from dRICH prototype
Data from INFN characterization
Data from INFN characterization
EIC PID Review - 5th July 2023

## Slide 16
dRICH Simulation: Resolution
16
Preliminary optimization of the dRICH optics inside EPIC
Magnetic field and track resolution accounted for, results averaged over azimuthal angle (f)
With single mirror, best focalization in the most demandig 2.5-3.5 pseudo-rapidity range to get ~ 0.3 mrad resolution
> 3s separation in the wanted momentum range (i.e. at maximum momentum)
EIC PID Review - 5th July 2023

## Slide 17
dRICH Simulation: Momentum reach
17
Momentum reach
Interplay between radiators
EIC PID Review - 5th July 2023

## Slide 18
R&D: Status
18
GEM
GEM
MAPMTs
Aerogel
Gas Vessel
Expected SPE ~ 1 mrad
Expected SPE ~ 3 mrad
Operative prototype commissioned. Double ring imaging achieved. Performance in line
with expectations except for aerogel single-photon angular resolution (worse by a factor ~ 1.5)
Gas ring coverage: 60%
Aerogel ring coverage: 40 %
Reference readout from CLAS12 RICH:
H13700 MA-PMTs + ALCOR3 ToT chip
Optics at variance with respect EIC
EIC PID Review - 5th July 2023

## Slide 19
R&D: Highlight
MPPC arrays selected with irradiation campaign
Front-end re-design completed
ALCOR v2 (bwetter dynamic range and rate)
ToT architecture, streaming mode ready
50 ps time bin
500 kHz rate per channel
cryogenic compatible
Hamamatsu S13361-3050
ALCOR chip
New EIC-driven readout unit
Realization of a suitable detector plane for the dRICH prototype (23/10): Design ready, procurement aligned to 2023 test-beam campaign.
Streaming readout
Integrated Cooling/ In-situ annealing
19
2023:
1 RDO per chip
2024:
1 RDO per PDU
Development
Kit KC705
Cooling plate
Peltier cells
Annealing circuitry
Multi-wafer run done
Version2:
32 channels
Extended dynamic range
Improved digital time
8x8 array
50 mm cell
Excellent fill factor
Best DCR
S14160 alternative
EIC PID Review - 5th July 2023

## Slide 20
R&D: Milestones
20
2023: EIC-driven detector plane
Initial characterization of realistic aerogel
and mirror components (23/04);
Projected performance of the baseline detector
as integrated into EPIC (23/06);
Assessment of the dRICH prototype performance
with the EIC-driven detection plane (23/10).
2024: Real-scale prototype for TDR (1 sector)
Mechanical structure
Realistic optics (off-axis)
ALCOR64 FEB + RDO
Aerogel and mirror demonstrator
New EIC-driven readout unit
Slide 8
Slide 16
Slide 19
Test beam planned in August and October 2023
EIC PID Review - 5th July 2023

## Slide 21
dRICH Construction Schedule
21
Aerogel may require longer engineering to reach the best performance (e.g. mass production efficiency)
SiPM may require longer engineering to reach the best performance (e.g. match temperature treatments)
Readiness planned 2 years before installation might result in a too aggressive schedule (see above)
EIC PID Review - 5th July 2023

## Slide 22
Optimization and Risk Mitigation
22
Component | Baseline | Optimization | Possible improvement
SiPM | Hamamatsu H13361-3050HS | 75 mm cell FBK sensor | Larger PDE Better time resolution
Aerogel radiator | Aerogel Factory n=1.02 | Refractive index Tile dimensions Tsinghua aerogel | Increase photon yield Reduce edge effects Risk reduction for single vendor
Gas radiator | SIAD C2F6 | Gas mixture Early procurement | Reduced environment impact (global warming) Limit dependence on market & regulations
Mechanics | Tecnavan Carbon fiber composite | Al composite | Cost reduction
Mirrors | CMA Carbon fiber composite | Mandrel material Different core strucuture Tessellation | Better shape quality vs cost
Cooling | Al plate | Carbon foam plate | Reduce material budget
EIC PID Review - 5th July 2023

## Slide 23
Environment, Safety & Health
23
1 year typical C2F6 losses would correspond to 1 intercontinental flight CO2 emission
requires to minimize losses in the recirculating system
About 2-2.5 kW per detector box
requires liquid cooling, dry air circulation + interlock
On-site annealing requires single-sensor temperature (optical) control
Low-T coolant circuit (down to -50 C) requires proper circuit and insulation
Thin transparent septa require delta-pressure control and safety diaphragms
EIC PID Review - 5th July 2023

## Slide 24
Quality Assurance
24
Aerogel: Refractive index, dimensions, defects, transmittance
organized within RICH Consortium (INFN-FE, INFN-BA, CERN, Temple)
https://docs.google.com/document/d/1YpN7gx85JjoQnoB9NblD61N9B1YhRGwBh2GIKZ2ST-0/edit
Mirror: Dimensions, shape accuracy, radius, reflectivity
JLab existing test laboratory with INFN-equipment, DUKE laboratory
Sensors: Electrical connections, quench resistor, I-V characteristics, DCR, relative PDE
Test stations in Italy (INFN-BO, INFN-FE, INFN-CS)
Front-end: Electrical connections, time jitter, ToT characteristics
Test stations in Italy (INFN-BO, INFN-TO)
Gas: Performance with prototype, transparency, contaminants
CERN
EIC PID Review - 5th July 2023

## Slide 25
Calibration and Commissioning
25
Detector response:
LED/laser system (sensor response and mirror alignment)
Dark count rate monitor
Single-photon time over threshold
Time calibration:
Absolute time with respect bunch crossing and Forward TOF
Time intercalibration: photons hits from the same event
Particle identification:
Control particle samples (identified by other systems)
Known meson decays (Ks, L, F)
EIC PID Review - 5th July 2023

## Slide 26
Executive Summary
26
Dual-radiator RICH is a cost-effective and compact solution for the forward PID at EPIC
Baseline configuration and technology has been identified to reach the EIC requirements
3s angular separation for forward hadrons up to 50 GeV/c momentum and up to 3.5 in pseudo-rapidity
dRICH Collaboration is setting up and an Executive Office has been enganged
R&D is on track to deliver the anticipated milestones towards TDR
Working on consolidating the baseline design with further optimization of the components
Need to integrate and validate all the progresses with a real-scale prototype prior of TDR
Aerogel and SiPM might need longer engineering (contingency) to reach the best performance
EIC PID Review - 5th July 2023

## Slide 27
Backup
27
EIC PID Review - 5th July 2023

## Slide 28
ALCOR Chip
28
EIC PID Review - 5th July 2023
Notes: LSB less significant bit

## Slide 29
ALCOR Chip
29
EIC PID Review - 5th July 2023

## Slide 30
Mirror Coating
30
EIC PID Review - 23th June 2023
Positive experience with ECI and carbon fiber substrace (CLAS12 RICH)
Custom evaporating facility at Stony Brook
Test Station @ JLab
Thorlabs compact spectrometer

## Slide 31
SIDIS Simulation
31
EIC PID Review - 23th June 2023
Old dRICH geometry
Similar to EPIC
Decent results with
likelihood PID
Notes: Aggiungere distribuzioni in numero fotoni ?

## Slide 32
Dew Point
32
EIC PID Review - 23th June 2023
Oil free dry-air compressors
- can reach 3% RH
- large air flux, up to 1200 l/min
Notes: Aggiungere distribuzioni in numero fotoni ?

## Slide 33
Executive Summary
33
EIC PID Review - 23th June 2023

## Slide 34
dRICH Vessel
34
EIC PID Review - 23th June 2023
Windows: sandwich panel made of two ~1 mm carbon fiber reinforced epoxy skins separated by 30 mm PMI foam or Al honeycomb (~ 1% X0)
Shells: 3 mm (inner tube) to 8 mm (outer tube) thick carbon fiber epoxy composite (~ 4% X0)
Skins formed with two layers of balanced weave laminate with fibers at 0o/90o and +/- 45o for uniform stiffness
Clearance vs support ring
Clearance vs beam pipe
Clearance
for services
1950
1270
Notes: Aggiungere distribuzioni in numero fotoni ?

## Slide 35
Prototype  dRICH
N x 0.7 QE spectrum
x 1.7 ring coverage
s x 0.9 N. photons
MA-PMT vs SiPM
35
EIC PID Review - 23th June 2023
Aerogel
Gas
Prototype  dRICH
N x 2.5 ring coverage
s x 0.7 QE spectrum
x 0.7
x 0.6 N. photons
No track resolution
Notes: Aggiungere distribuzioni in numero fotoni ?

## Slide 36
Dew Point
36
EIC PID Review - 23th June 2023
Notes: Aggiungere distribuzioni in numero fotoni ?