## Slide 1
eRD14 – EIC PID consortium
- An integrated program for particle identification (PID) for a future Electron-Ion Collider (EIC) detector.
M. Alfred, B. Azmoun, F. Barbosa, L. Barion, W. Brooks, T. Cao, M. Chiu, E. Cisbani, M. Contalbrigo, S. Danagoulian, A. Datta, A. Del Dotto, M. Demarteau, A. Denisov, J.M. Durham, A. Durum, R. Dzhygadlo, C. Fanelli, D. Fields, Y. Furletova, C. Gleason, M. Grosse-Perdekamp, J. Harris, M. Hattawy, X. He, H. van Hecke, T. Horn, J. Huang, C. Hyde, Y. Ilieva, G. Kalicy, A. Kebede, B. Kim, E. Kistenev, M. Liu, R. Majka, J. McKisson, R. Mendez, I. Mostafanezhad, P. Nadel-Turonski, K. Peters, R. Pisani, W. Roh, P. Rossi, M. Sarsour, C. Schwarz, J. Schwiening, C.L. da Silva, N. Smirnov, J. Stevens, A. Sukhanov, X. Sun, S. Syed, R. Towell, G. Varner, R. Wagner, C. Woody, C.-P. Wong, W. Xi, J. Xie, Z.W. Zhao, B. Zihlmann, C. Zorn.
Contacts:
P. Nadel-Turonski <turonski@jlab.org>,
Y. Ilieva <jordanka@physics.sc.edu>
Generic Detector R&D for an Electron Ion Collider
Advisory Committee Meeting, BNL, January 24-25, 2019

## Slide 2
Dual-radiator RICH (dRICH)
Goal:
Progress in 2nd half of 2019:
  Prototyping
    Consolidated prototype design
    Started procurement of prototype components
  Finalized Bayesian Optimization Method for detector design, tested on dRICH
  Detailed analysis of the event-based reconstruction algorithm performance
Provide hadron identification (p/K/p) from 3 to 50 GeV/c (3 sigma) and electron identification (e/p) up to 15 GeV/c, in the forward ion-side endcap of the EIC detector, covering polar angles up to ~25 deg.

## Slide 3: dRICH in EIC - baseline model
Radiators: Aerogel (4 cm, n(400nm)1.02) + 3 mm acrylic filter, Gas (1.6 m, nC2F61.0008)
6 Identical Open Sectors (Petals):
  Large Focusing Mirror with R 2.9 m
  Optical sensor elements: 4500 cm2/sector, 3 mm pixel size, UV sensitive, out of charged particles acceptance
Sensor Surface
Spherical Mirror
Aerogel
Hits on detector
Photon impact
on mirror(s)
Gas
Advantages:
Full momentum, continuous coverage
Relatively simple geometry/optics
Expected to be Cost Effective (respect to 2 x detectors solution)
Available:
detailed simulation model including photon scattering in aerogel and 3 T central magnetic field
event-based reconstruction
Demand excellent performance from aerogel!

## Slide 4
dRICH Performance Optimization
Combine detailed MonteCarlo simulations with Bayesian Approach to efficienty maximize a proper Figure of Merit (p-K Cherenkov angles separation in critical phase spaces regions, e.g. aerogel-gas transitions, high momentum limit …)
Current implementation uses 8 independent parameters (can be extended easily) 
The method provides optimized performances and hints on relevance of different detector features
It can be ported to any detector development (or combination of detectors) where detailed MonteCarlo exists
arXiv:1911.05797 submitted to JINST

## Slide 5
dRICH prototype (a new detector …)
Design in an advanced stage, mechanical details being finalized
Standard Vacuum Technologies to optimize gas handling
Two tuneable mirrors system for using the same detector
Common (limited) sensitive surface for both aerogel and gas photons
Detector and aerogel box isolated from the gas tank

## Slide 6
Activity | T1 | T2 | T3 | T4
Prototype Component procurement |  |  |  | 
Prototype construction |  |  |  | 
Prototype simulation analysis |  |  |  | 
Prototype lab test |  |  |  | 
Aerogel-gas long term test |  |  |  | 
Sensor characterization (mRICH + dRICH) |  |  |  | 
Electronics test and integration (mRICH + dRICH) |  |  |  | 
Important components (electronics and sensors) of the dRICH prototype are shared with the mRICH development
CLAS12 infrastructures available in Ferrara/JLab is used for aerogel-gas studies and photon sensors characterization
FY20 outlook
Contract awarded for mechanics and aerogel, funds secured for mirror system and
at least the cheaper freon gas. Sensor characterization campaign initiated.