## Slide 1
Goals:
Provide a reference readout system for prototypes performance assessment
Developed a generic DAQ system compatible with the Consortium needs
Test applications with innovative sensors (SiPM)
Progress in 2nd half 2018 on:
3 mm2 pixel readout compatibility (H13700 and SiPM)
Pulsed laser test benches for detailed characterization
Radiation tolerance study for SiPM
ELECTRONICS
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 2
Derived from CLAS12 RICH readout:
1024 channels
MAROC 64 channel parallel digitalization
FPGA generated 1 ns timestamp
DAQ protocol based on VME/VSX SSP
Custom adapter boards
- Compact distribution
Use of existing MAROC boards
Light and gas tightness
H13700 READOUT
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 3
3
Contalbrigo M.
SiPM might offer a cheaper and more efficient solution, expecially in a longer time perspective for other sectors
Robust device with low sensitivity to magnetic field
Fast improvement in dark rate and cost
but so far missing radiation hardness
Challenge: cooling integrated into the sensitive readout
Custom cooling plate
Soldered to the board
Peltier cell cooling
Down to -30o in N2
eRD14 PID Consortium – 01/07/19
Dedicated board for readout and cooling
of a surface Mounting SiPM Matrix
SIPM READOUT
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 4
Paolo Carniti
@ RICH 2018
I. Balossino et al.
NIMA 876 (2017) 89
SIPM RADIATION TOLERANCE
T. Tsang et al.
JINST 11 (2016) P12002
T= 84 K
109 neq cm2
Annealing at 250 oC
T= 0 C
few 109 neq cm2
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 5
Laser head +
diffuser
MAPMT holder
JLab
632 nm picosecond pulsed laser light
Light diffuser to illuminate the whole MAPMT surface
Standardized system with CLAS12 electronics
H8500 6x6 mm2 pixel sensor so far
Ferrara
632 nm and 407 nm picosecond pulsed laser light
Light concentrator to scan the pensor surface
Flexible layout supporting various sensors and
Front-End electronics
Detailed characterization
Sensors: gain, efficiency, cross-talk, radiation tolerance
Electronics: gain, cross-talk, thresholds, time resolution
Laser head +
collimator
MAPMT holder
PULSED LASER TEST BENCHES
Notes: Fare una immagine del PMT sulla risoluzione