## Slide 1
The Large-area Hybrid-optics CLAS12 RICH: First years of Data-Taking
M. Contalbrigo – INFN Ferrara – on behalf of the CLAS12 RICH group
RICH2022 - 11th International Workshop
on Ring-imaging Cherenkov Detectors
12th September 2022,
University of Edinburgh
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 2
2
Contalbrigo M.
CLAS12
RICH2022, 12th September 2022, Edinburgh
Large acceptance spectrometer. Operative since 02/18
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 3
3
Contalbrigo M.
RICH @ CLAS12
RICH2022, 12th September 2022, Edinburgh
Completed in June 2022 with the symmetric configuration dedicated to the runs with polarized targets (now ongoing)
1
2
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 4
4
Contalbrigo M.
CLAS12 RICH
RICH2022, 12th September 2022, Edinburgh
INSTITUTIONS
INFN (Italy) Bari, Ferrara, Genova, L.Frascati, Roma/ISS
Jefferson Lab (Newport News, USA)
Argonne National Lab (Argonne, USA)
Duquesne University (Pittsburgh, USA)
George Washington University (USA)
Glasgow University (Glasgow, UK)
Kyungpook National University, (Daegu, Korea)
University of Connecticut (Storrs, USA)
UTFSM (Valparaiso, Chile)
Cherenkov angle (mrad)
7 Gev/c
6 Gev/c
8 Gev/c
p
k
p
Goal kaon-pion separation up to 8 GeV/c (prototype results):
Direct imaging
aerogel
mirrors
detector
4 m
Double
reflection
@RICH2013
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 5
5
Contalbrigo M.
Aerogel
RICH2022, 12th September 2022, Edinburgh
RICH2 – 3 cm layer
RICH2 – 2 cm layer
In line with R&D achievements
RICH1
n=1.05, 20x20x3 cm3 aerogel tiles produced by the Budker and Boreskov Institutes of Novosibirsk
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 6
6
Contalbrigo M.
Aerogel Assembling
RICH2022, 12th September 2022, Edinburgh
Hydrophilic & shaped by machine cutting: handling care, mechanically and optically isolated by thin foam strips
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 7
7
Contalbrigo M.
Mirrors
RICH2022, 12th September 2022, Edinburgh
Glass-Skin Mirrors (planar) - Media-Lario, IT
Innovative technology never used in nuclear experiments (foils of 1.5 mm outside, 0.7 mm inside acceptance)
~ 1/5 cost for squared meter vs CFRP, surface defects (from dust on mold) within specifications
Carbon Fiber Mirrors (spherical) - Composite Mirror Applications, USA
to maximize lightness and stiffness. Consolidate technology (HERMES, AMS, LHCb)
~ 20 % material budget reduction vs precedents, radius and shape better (RICH1) or comparable (RICH2) than specs
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 8
8
Contalbrigo M.
Mirror Assembling
RICH2022, 12th September 2022, Edinburgh
Use of composite CFRP and Al materials (Tecnologie Avanzate, IT) to realize a light but stiff supporting structure
Mounting
Alignment
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 9
9
Contalbrigo M.
Photon Detector
RICH2022, 12th September 2022, Edinburgh
Readout Electronics
Compact, modular (adapter, MAROC3, FPGA) and scalable
Hamamatsu H12700 (+ H8500)
< 1 cm spatial resolution
< 1 ns time resolution
Compatible with the low torus fringe field
Average gain ~ 2.7 106
eq. to SPE ~ 400 fC
Threshold: Fraction (<10%) of SPE
Trigger latency (8 ms)
Optical ethernet (2.5 Gbps)
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 10
10
Contalbrigo M.
Pedestals
RICH2022, 12th September 2022, Edinburgh
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 11
11
Contalbrigo M.
Gain Equalization
RICH2022, 12th September 2022, Edinburgh
MAROC: ToT in an almost saturated regime
Pixel-by-pixel gain variation is compensated
by the front-end amplification stage
With equalization:
The plateau vs threshold is extended
Threshold at 25 DAC ( ~5 % SPE)
RICH1
RICH2
Dark counts
Dark counts
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 12
12
Contalbrigo M.
Dark Counts
RICH2022, 12th September 2022, Edinburgh
100 Hz
1 kHz
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 13
13
Contalbrigo M.
Dark Rate
RICH2022, 12th September 2022, Edinburgh
PMT 341
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 14
14
Contalbrigo M.
Dark Rate
RICH2022, 12th September 2022, Edinburgh
PMT 118 Anode 57
Problematic channel:
DR above 1 MHz
Going to saturation
Cross-talk on neighbors
PMT 266 Anode 2
Problematic channel:
Initial DR 13 Hz
Increasing to 4 kHz
High-dark rate channels
RICH1 ~ 10
RICH2 none so far
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 15
15
Contalbrigo M.
Time Walk
RICH2022, 12th September 2022, Edinburgh
ns
ns
Run 5038 – Oct 18
Run 11328 – Jan 20
D0
m1
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 16
16
Contalbrigo M.
Time Calibration
RICH2022, 12th September 2022, Edinburgh
RICH time calibration with CLAS12 time-of-flight detector + bunch crossing
ch
ch
Requested to tag double reflections
DT (ns)
(ns)
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 17
17
Contalbrigo M.
Cross-Talk
RICH2022, 12th September 2022, Edinburgh
Optical
Electrical
Optical
& Electrical
Analysis based on topology and signal shape
Optical
Electrical
Signal
Residual cross-talk is removed after time calibration with TOF
Hit
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 18
18
Contalbrigo M.
Photon Path Reconstruction
RICH2022, 12th September 2022, Edinburgh
From CLAS12:
particle momentum
photon emission point
From RICH:
hit time and position
Direct ray-tracing:
ray-trace a limited sample of photon trials
(selection of f’s for given q)
adjust the angles to match the hit
starting from the closest trial
(convergence in 2-3 iterations)
validate photon reconstructed
Cherenkov angle and transit time
q
DC track
RICH hit
Trial
f
Complex geometry with various photon paths
(reflections) off the same particle
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 19
19
Contalbrigo M.
Pattern Recognition
RICH2022, 12th September 2022, Edinburgh
Photon path reconstruction allow to assign the photon to the most likely hypothesis:
- be robust and easy to control (easy to handle multi-reflections, up to e.g. 5)
- discriminate background (hit far from trials, no solution foreseeable)
- provide full information (photon path, time, position and component of each reflection)
- allow relation with nominal optical components, resolution and efficiency
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 20
20
Contalbrigo M.
Alignment & Resolution
RICH2022, 12th September 2022, Edinburgh
Direct photons: electrons vs pi+
Before alignment
After alignment
Electrons: direct vs planar reflection
Electrons: direct vs spherical reflection
Alignment requires large statistics and full reconstruction to deal with the various photon paths
Angular resolution is comparable for direct and reflected photons
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 21
21
Contalbrigo M.
Angular Resolution
RICH2022, 12th September 2022, Edinburgh
The goal of a pion-kaon 4s separation at 8 GeV/c requires a resolution of 1.5 mrad*
(*forward region, less stringent requirements at large angles)
In line or better with respect the TDR targets:
- single-photon resolution of 4.5 ns
- number of photons around 18 for direct imaging
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 22
22
Contalbrigo M.
Particle Identification
RICH2022, 12th September 2022, Edinburgh
epep+n
background
epeK+L
signal
Check with semi-inclusive physics channel epeh+X
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 23
23
Contalbrigo M.
Conclusions
RICH2022, 12th September 2022, Edinburgh
CLAS12 RICH designed to provide hadron identification in the 3 to 8 GeV/c momentum range
A hybrid-optic design has been adopted to minimize the instrumented area to about 1 m2
Featuring:
- aerogel with status-of-the-art transmittance and unprecedented volume at n=1.05
- carbon fiber spherical mirrors with reduced material budget
- cost-effective glass-skin planar mirrors used for the first time
- large-area multi-anode photomultipliers adopted for the first time
- modular front-end electronics easy to adapt for other applications
(in use for GlueX DIRC, SOLID R&D, EIC dRICH R&D)
Discrimination down to few % of SPE
Time resolution of 1 ns
Negligible dead time at 30 KHz
Trigger latency up to 8 ms
RICH has successfully taken data, performance approaching specifications and supporting physics analysis
Notes: Vanno messi studi innovativi e pubblicazioni