## Slide 1
Particle Identification
Lesson 2 - Methods
M. Contalbrigo – INFN Ferrara
2nd European School on the Physics of the EIC and Related Topics, 22th June – 2nd July, 2025
1
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo

## Slide 2
Arguments
2
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
Specific Particle-ID Detectors Time-of-Flight
Cherenkov Radiation
Reconstruction example
Analysis Methods Chi2
Maximum Likelihood
Machine Learning techniques
ePIC Requirements
ePIC Solutions pfRICH
TOF
hpDIRC
dRICH
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 3
p = g m bc
Process | Particle | Equipment
Energy Loss (dE/dx) | Hadrons | Tracking
Transition Radiation (TDR) | Electrons | Tracking sensitive to X-ray
Time-of-Flight (TOF) | Hadrons | Timing
Cherenkov Radiation | Hadrons | Cherenkov
PID by Tracking
Assume to know the momentum (by tracking the bending in a magnetic field)
Get the mass by measuring the velocity (bc)
3
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo

## Slide 4
The T0 Problem
4
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
In a time of flight application one needs two layers (impractical) or a reference t0
with better (or comparable) precision with respect TOF.
The t0 is typically given at the interaction point by back-tracking:
- Reference particle (e.g. lepton in deep-inelastic scattering)
- Average over particles (requires large multiplicity)
- Bunch RF information (require to “just” identify the beam bunch crossing)

## Slide 5
Cherenkov Radiation
Momentum threshold:
Photon yield:
Scales with particle mass
Decreases with n
5
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo

## Slide 6
Photon Yield
Spectrum of Cherenkov photons
Typical sensitivity (quantum efficiency) of a PMT
4 eV
2 eV
3 eV
4 eV
2 eV
3 eV
6
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo

## Slide 7
Cherenkov Radiators
~ 1 m
~ few cm
Real PID
starts at
3x (kaon)
(1.015-1.08)
7
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
~1 keV/cm
10-3 dE/dx
requires
requires
ePIC
COMPASS / LHCb
BELLEII / CLAS12

## Slide 8
Photon Detection
8
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
Photon detector
Proximity focusing
Focusing mirror

## Slide 9
Chromatic Dispersion
9
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
X
Refractive index as a function of the Cherenkov light wavelength for the aerogel with n = 1.05 and trad = 20 mm obtained selecting pions with 8 GeV/c momentum.
Gas Radiator
Aerogel Radiator
X
Sellmeier parameterization

## Slide 10
Cherenkov Resolution
sco correlated uncertainty (tracking, misalignment, magnetic bending, multiple scattering, ….)
sem uncertainty on the photon emission point (radiator depth)
sch radiator chromatic dispersion (uncertainty on the photon wavelength)
spx sensor spatial resolution (pixel size)
Q(l) Sensor quantum efficiency epe detection efficiency (sensor and mirror)
L(l) Radiator transmission length trad radiator thickness
10
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo

## Slide 11
BELLE ARICH
11
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
1.045
1.055
17 cm
D0--> K-p+ 0.5 - 3.5 GeV/c
Limited space --> Proximity focusing & radiator focusing
High B field (1.5T) --> Custom Hybrid photon detector
Super bialkali photocatode
Gain 4.5 106
PDE ~ 28 %
BELLE-II: B-factory

## Slide 12
X
CLAS12 RICH
12
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
X
Electrons: direct vs spherical reflection
95 % kaon efficiency
(<1% pion mis-ID) up to 8 GeV/c
CLAS12: Nucleon structure
and spectroscopy

## Slide 13
LHCb RICH
LHCb Precisin measurements of B-decays
and search fro BSM signals
RICH1: Aerogel (5 cm) n=1.03
2-10 GeV/c
C4F10 (85 cm) n=1.0014
up to 70 GeV/c
RICH2: CF4 (196 cm) n=1.0005
up to 100 GeV/c
Hybrid photomultiplier
Photocatode @ - 20 kV
Silicon sensor
LHCb B physics
RICH1
13
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo

## Slide 14
X
X
X
X
DIRC
2D imaging - Babar
1D + time maging – Belle-II
Detection by internal reflection: compact detection volume (thickness)
Critical aspects: quartz surface quality (parallelism, roughness)
proper imaging system
Air
Babar
Belle-II
B factory
B factory
14
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo

## Slide 15
CsI Photocatode
15
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
Large instrumented area
Multi-wired proportional chambers with a CsI photocatode
Quantum efficiency is around 16-24% at 170 nm
High-Momentum PID
RICH
A = 5.3 m2
A = 11 m2
ALICE: Quark-gluon plasma in heavy ion collisions
COMPASS: Nucleon structure and spectroscopy

## Slide 16
Cosmic Rays
A cosmic gamma ray generates a particle shower in the atmosphere
Showering charged particles generates Cherenkov radiation
The number of detected photons is proportional to the initial energy
Air refractive index is n = 1.00028
Threshold energy is 4.4 GeV for muons and 21 MeV for electrons
Cherenkov angle is 23 mrad ~ 1.3o
The shower maximum is at 10 km and generates a cone of 230 m
Extended detection pattern in
space and time gives the direction
16
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo

## Slide 17
17
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
PID Reconstruction

## Slide 18
CLAS12 RICH
18
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
Direct imaging
aerogel
mirrors
detector
Double
reflection
Hamamatsu H12700 (+ H8500)
< 1 cm spatial resolution
< 1 ns time resolution
Average gain ~ 2.7 106
eq. to SPE ~ 400 fC
Goal: Hadron identification rom 3 GeV/c up to 8 GeV/c
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 19
Geometry
19
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 20
Time
20
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
TOF
(t0)
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 21
Ray Tracing
21
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
and time
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 22
Convergence
22
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 23
Reconstruction
23
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 24
24
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
PID Analysis

## Slide 25
Analysis
25
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
Least squares
minimization
Likelihood
maximization
Machine learning
techniques
Signal
Signal
Probabiliy
Probabiliy
p
k
p
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 26
Particle Identification
26
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
dE/dx
TRD
TOF
Best performance is with an holistic approach
Correlating featured signals from the same detector (dE/dx points, TRD layers, ring photons,….) or from different detectors
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 27
Holistic Approach
27
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
TRD
TOF
RICH
dE/dx
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 28
Observe n events xi and expect a total of m
In the logL any constant is irrelevant, i.e. any term that does not depend
on the parameters q.
In case f(xi;q) is a binned PDF with poisson probability the above reduces
(except for a constant) to the binned maximum likelihood
L
Extended Maximum Likelihood
28
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 29
Taking a likelihood ratio, vs an ideal model corresponding to the measurement
(mi=ni), provides a chi2-like estimator (goodness of fit) if mi are not too small
* mi is the expected yield in bin i (signal + background)
* pdf normalization to 1 is given by Poisson
* the mi – ni term is optional (less stringent except close to threshold)
* one can have bins with zero counts (last term is taken to be zero)
Extended Maximum Likelihood
29
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 30
All these quantities are defined at pixel level
- dq and df are known by RICH reconstruction.
- e(i) can reflect dead (0) or hot (1) channels, or the quantum/reflection efficiency ([0:1])
- B(i) can be derived from random triggers or electron control sample
Reference values could accounts for second order effects
(photon path and pattern change among various mass hypotheses).
Flat
probability
t may change due to
path (direct or reflected)
Measured values
Cherenkov Example
30
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
+ B(i)
B
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 31
Should reduce to a sort of chi2.
Beyond non gaussian effects and the optional normalization term, the difference is in the
background that defines a sort of cutoff: an accepted hit that is background for all the
hypotheses does not count in the likelihood, whereas the ordinary chi2 weights anyway its
distance from the expected value (provides a preference) except it is explicity excluded
Likelihood Ratio
31
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
One might take the likelihood ration with he model corresponding to the
“observed measurement” in which all the hit are at the right (expected) angle
t=ti
q=qi
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 32
Without 2(Nexp-N) term
Extended Maximum Likelihood
32
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 33
With 2(Nexp-N) term
Extended Maximum Likelihood
33
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 34
Neural Networks
34
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
Features of data
Identification
Classifier
p
k
Connection: got a weight defining the strenght
Node: got an activation function for the output value from weighted inputs plus bias
Connection
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 35
NN Training
35
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
Classifier
p
k
Connection: got a weight defining the strenght
Node: got an activation function for the output value from weighted inputs plus bias
During iterative learning, the network parameters are automatically tuned on training samples
to minimize the difference between estimate and correct answer in several cycles (epochs)
Connection
p
k
p
k
Features of data
Identification
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 36
Neural Networks
36
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
Features of data
Identification
Classifier
p
k
The network is then ready to classify sets of data and represents a correlation map over distinctive features
Potential biases: relevance of the features, should bring discrimination power
type of classifier, should provide enough flexibility (e.g. node and layer number
goodness of training, should provide an acceptable convergence
training sample, pseudo-data should reflect the real data features
Connection
p
k
?
Critical as assumes an
a-priori knowledge
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 37
Analysis
37
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
Least squares
minimization
Likelihood
maximization
Machine learning
techniques
Signal
Signal
Probabiliy
Probabiliy
p
k
p
Signal
Population
p
k
p
Correlations via covariance matrix
Correlations via multi-D p.d.f.
Correlations via NN training
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 38
Patter Recognition
38
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
TOP BELLEII
p
k
p
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 39
Online Filtering
Scheme based on ePIC DAM (Felix) &
APEIRON communication network (INFN)
Preliminary tests
detector integrated analysis
sub-sector integrated analysis
Classifier
Efficiency increase (resources saving) when useless degrees of freedom are removed, i.e. the NN architecture is aligned to the real detector layout
39
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
Notes: Farsi spieare la latenza. Bisogna sapere ul data rate a cui sono arrivati (factor 2?)

## Slide 40
40
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
ePIC PID Requirements

## Slide 41
ePIC Detector
41
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
h (275 GeV)
e (18 GeV)
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 42
ePIC Environment
42
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
Magnetif field
Radiation Map
(1 MeV eq. neutron
fluence cm-2 fb-1)
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 43
43
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
ePIC PID Solutions

## Slide 44
Goals:
Hadron 3s-separation up to 7 GeV/c
Complement electron ID below 3 GeV/c
Cover forward pseudorapidity -3.5 : -1.5 (e-endcap)
dRICH Features:
Limited space --> Simple geometry, gap minimized
Precise time information --> HRPPD
Single-photon detection in high Bfield --> HRPPD
ePIC pfRICH
Proximity-Focusing Ring-imaging Cherenkov Detector (pfRICH)
Essential to access flavor information
44
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo

## Slide 45
HRPPD
45
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
Gain uniformity
A.V. Lyashenko e-Print: 2505.10658
l = 365 nm
Average QE (5 over 7)
C. Chatterjee PoS DIS2024 (2025) 266

## Slide 46
Goals:
Hadron 3s-separation up to 1.2 Gev/c (barrel)
Hadron 3s-separation up to 2.5 Gev/c (h-endcap)
Cover mid-forward pseudorapidity -1.5 : 3.5
dRICH Features:
Precision in limited space --> silicon detector
Up to 2.5 GeV/c momentum range --> AC-LGAD
Coplement tracking --> AC-LGAD
ePIC TOF
Time-of-Flight Detector (TOF)
Essential to access flavor information
46
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo

## Slide 47
AC-LGAD
47
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
C. Chatterjee PoS DIS2024 (2025) 266
LGAD adds a p+ layer with large Boron doping to create
a region of high field and concentrated avalanche
AC-coupling allows space precision without
affecting the uniformity of the gain layer
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 48
Goals:
Hadron 3s-separation between 3 - 6 GeV/c
Complement electron ID below 1.2 GeV/c
Cover forward pseudorapidity -1.5 - 1.5 (barrel)
dRICH Features:
Limited space --> Internal reflection
Up to 6 GeV/c momentum range --> Lens
Single-photon detection in high Bfield --> MCP-PMT
ePIC hpDIRC
High-Performance (dRICH)
Essential to access flavor information
48
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo

## Slide 49
ePIC hpDIRC
49
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
Re-use of BABAR DIRC bars and cosmic test
Quartz prism with focalizing sapphire lens
Compact, high-performance (+50%) design
G. Kalicy NIMA 1062
(2024) 169168
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 50
Goals:
Hadron 3s-separation between 3 - 50 GeV/c
Complement electron ID below 15 GeV/c
Cover forward pseudorapidity 1.5 - 3.5 (h-cap)
dRICH Features:
Extended 3-50 GeV/c momentum range --> Dual radiator
Single-photon detection in high Bfield --> SiPM
Limited space --> Compact optics with curved detector
ePIC dRICH
Dual-radiator Ring-imaging Cherenkov Detector (dRICH)
Essential to access flavor information
4m
50
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo

## Slide 51
c. Chatterjee DIS2024 (2025) 266
ePIC dRICH
51
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
C. Chatterjee PoS DIS2024 (2025) 266
Imaging study
Annealing study
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 52
ePIC PID System
52
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
Precise timing with HRPPD
+50% momentum reach with lens
Detectionin in high
B-field with SiPM
Precise tracking by AC-LGAD
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 53
Arguments
53
2nd European School on EIC Physics, 22th June – 2nd July, 2025
M. Contalbrigo
Specific Particle-ID Detectors Time-of-Flight
Cherenkov Radiation
Reconstruction example
Analysis Methods Chi2
Maximum Likelihood
Machine Learning techniques
ePIC Requirements
ePIC Solution pfRICH
TOF
hpDIRC
dRICH
Notes: Vanno messi studi innovativi e pubblicazioni